## Slide 1: Recent Efforts of the MPI Forum for MPI-4 and Future MPI Standards
Pavan Balaji
Argonne National Laboratory
Howard Pritchard
Los Alamos National Laboratory
LA-UR-19-20284

## Slide 2: MPI-4 Standardization Process
Multiple working groups, each working on individual topics
  Fault Tolerance, Persistence, One-sided Communication, Sessions, …
Beginning in 2018, started holding monthly virtual forums to speed up standardization process
MPI-4 2018 draft standard released in Nov. 2018
  Some features have already been voted in
  The standard as a whole has not been voted in yet (it’s not yet “MPI-4”)
Final MPI-4 is expected to be out in around 2 years

## Slide 3: Fault Tolerance
MPI_ERRORS_ABORT: Added new predefined error handler which only causes processes in the affected communicator to abort
Errors_Abort
User Level Failure Mitigation
Non-Catastrophic Errors
After an error is detected, the state of MPI is undefined.
MPI should return as much information as possible about errors.
  Gives users more control over how to handle errors.
  If you really want to, you could construct a resilient point-to-point-only application on top of this change.
This small change (along with the previous one), should actually provide enough error handling improvements to avoid application aborts during simple errors like resource exhaustion.
Enable application-level recovery by providing minimal FT API to prevent deadlock and enable recovery
Don’t do recovery for the application, but let the application (or a library) do what is best
Currently focused on process failure (not data errors or protection)
0
0
MPI_Send
Failure Notification
MPI_ERR_PROC_FAILED
0
1
3
2
Failure Propagation
Recv(1)
Failed
Revoke
Recv(3)
Recv(0)
Send(2)
Revoked
Revoked
Revoked
Failure Recovery
MPI_COMM_SHRINK()
MPI_ERRORS_ARE_FATAL
MPI_COMM_WORLD
NEW_COMM
Causes aborts everywhere
Error here
MPI_COMM_WORLD
NEW_COMM
MPI_ERRORS_ABORT
MPI_COMM_WORLD
NEW_COMM
Causes aborts only here
Error here
MPI_COMM_WORLD
NEW_COMM

## Slide 4: Persistence Collective Operations
MPI_Bcast_init(bufA, …, rowcomm, &req[0]);
MPI_Reduce_init(bufB, …, colcomm, &req[1]);
for (i = 0; i < MAXITER; i++) {
compute(bufA);
MPI_Start(req[0]);
compute(bufB);
MPI_Start(req[1]);
MPI_Waitall(2, req, …);
}
Nonblocking collectives API
Persistent collectives API
for (i = 0; i < MAXITER; i++) {
compute(bufA);
MPI_Ibcast(bufA, …, rowcomm, &req[0]);
compute(bufB);
MPI_Ireduce(bufB, …, colcomm, &req[1]);
MPI_Waitall(2, req, …);
}
Mirror regular nonblocking collective operations
For each nonblocking MPI collective, add a persistent variant
For every MPI_I<coll>, add MPI_<coll>_init
Parameters are identical to the corresponding nonblocking variant – plus additional MPI_INFO parameter
All arguments “fixed” for subsequent uses
Persistent collective operations cannot be matched with blocking or nonblocking collective calls
Has been voted in to Standard by the Forum

## Slide 5: Remote Memory Access (RMA)
MPI Generalized Atomics
MPI-3 atomic operations are, in some cases, restrictive and are not precisely defined
Two proposals:
  Clarify what operations are atomic and what are not (minor change)
  Allow for generality of atomic operations with room for performance optimization
Generality: Ability for different atomic operations to be issued on the same target location
Performance: Additional info hints to restrict what the user will use (e.g., only CAS, only FOP, only basic datatypes)
Neighborhood Communication in MPI RMA
MPI-3 defined neighborhood collectives as a process only communicates with its neighbors
Neighborhood RMA is a generalization of that concept to allow RMA to neighboring processes
  Allows MPI implementations to optimize state that is internally managed
  Primarily an optimization for memory usage (e.g., MPI does not need to store information about non-neighbor processes)
    Can also improve performance in some rare cases
In passive target mode, notifying the target that data has been transmitted is currently inefficient
Two proposals for target notification: 1) Notification on PUT/GET 2) Notification on Flush
Idea is to notify the target when the data has been deposited into the target public memory
RMA Notifications

## Slide 6: MPI Tools – Events Interface
Proto-type implemented in Open MPI
EuroMPI 2018 paper: Hermanns et al., Enabling callback-driven runtime introspection via MPI_T
Interface for tools to get notification of events occurring within an MPI implementation
No events defined explicitly in the standard
MPI implementation decides which events exposed through to MPI_T events interface and when
Callback interface used to notifies tools of an event occurrence
MPI_T Events

## Slide 7: MPI Sessions –
Different components of an application allocate MPI resources independently
MPI resources can be allocated/deallocated multiple times within a process
Introduces the notion of isolation of MPI resources allocated by different components of an application
Can be used with MPI applications that currently use MPI_Init/MPI_Finalize
MPI without the Init
Query runtime for set of processes, e.g. mpi://world
MPI_Group
MPI_Comm
MPI_Session
Proto-type Status
Proto-type implemented in Open MPI
Makes use of PMIx Groups API
https://github.com/hppritcha/mpi_sessions_tests

## Slide 8: Point-to-Point Communication
Communication Relaxation Hints
mpi_assert_no_any_tag
  The process will not use MPI_ANY_TAG
mpi_assert_no_any_source
  The process will not use MPI_ANY_SOURCE
mpi_assert_exact_length
  Receive buffers must be correct size for messages
mpi_assert_overtaking_allowed
  All messages are logically concurrent

## Slide 9: Hybrid MPI Programming
Hardware
Application
MPI
CTX
User Endpoint
Hardware
Application
MPI
CTX
User Endpoint
CTX
Hardware
Application
MPI
CTX
User Endpoint
CTX
User Endpoint
User Endpoint
Hardware
Application
MPI
CTX
User Endpoint
Most common current approach
  Single endpoint per MPI process
  Worst case contention
Possible optimization in MPI-3.1: multiple invisible endpoints
  Multiple internal endpoints (BG/Q style)
  Transparent to the user
  E.g. one endpoint per comm, per neighbor process (regular apps)
Endpoints proposal for MPI-4: multiple user-visible endpoints
  Multiple endpoints managed by the user
Idea is to have multiple addressable communication entities within a single MPI process
  Instantiated in the form of multiple ranks per MPI process
Each rank can be associated with one or more threads
Reduced contention for communication on each “rank”
In the extreme case, we could have one rank per thread (or some ranks might be used by a single thread)
MPI endpoints
Implementation phases/options